## Slide 1: MEF Modeling Approach For Discussion
Tara Cummings, Ericsson

## Slide 2: What is MEF LSO?
LSO defined in MEF Specification 55 and provides for the orchestrated management and control of Third Network Connectivity Services
LSO Reference Architecture characterizes the management and control domains and entities that enable the cooperative LSO capabilities
LSO overcomes existing complexity by defining product, service, and resource abstractions that hide the complexity of underlying technologies and network layers from the applications and users of the services
Orchestration
Connectivity Services are orchestrated across all internal and external network domains from one or more network operators
Encompasses all network domains that require coordinated end-to-end management and control to deliver connectivity services
Within each provider domain, the infrastructure may be implemented with WAN technologies, as well as NFV and/or SDN
Not only dramatically decreases the time to establish and modify the characteristics of the Connectivity Service, but also assure the overall service quality and security for these services.

## Slide 3: LSO Reference Architecture and Framework
Provides a layered architecture that characterizes the management and control domains and entities that enable the cooperative LSO capabilities for Connectivity Services.
High level operational threads describing user stories of orchestrated Connectivity Service behavior as well as interactions among management entities, expressing the vision of the MEF LSO capabilities
The management interface reference points that characterize interactions between LSO ecosystem components are identified in the reference architecture

## Slide 4: Potential LSO Alignment to IETF –for discussion
Network-A
Network-B
Network-C
PNC-A
PNC-B
PNC-C
Southbound Interface
(e.g. TL1, SNMP, CLI,
PCEP, NETCONF, etc.)
IETF Models
ONF Models
MEF ExtSpec Models
Multi-model
Northbound Interface
MDSC
(IETF, ONF, other SDO based internal model)
IETF Model
Mediator
ONF Model
Mediator
ONF Model Transport API
Model Translation/Mediation: For multi-model environment, deployment use case must be fully supported by all models.
  Model translation / mediation between systems using different models should be seamless.
Infrastructure Control and Management
Service Orchestration Functionality
Presto
Infrastructure Control and Management
Presto

## Slide 5: CURRENT approach for MEF Projects
E
SP Domain
Customer Domain
Partner Domain
Network Infrastructure
Customer
Application Coordinator
Element Control and Management
Infrastructure Control and Management
Service Orchestration Functionality
Presto
(SOF:ICM)
Allegro
(CUS:SOF)
LEGATO
(BUS:SOF)
Cantata
(CUS:BUS)
Element Control and Management
Infrastructure Control and Management
ADAGIO (ICM:ECM)
LEGATO
(BUS:SOF)
Presto
(SOF:ICM)
ADAGIO (ICM:ECM)
Interlude (SOF:SOF)
Sonata
(BUS:BUS)
Business Applications
Business Applications
Service Orchestration Functionality
REFERENCE ARCHITECTURE
CE Info Model (MEF 7.3)
Presto
Network Resource Provisioning (NRP Profile)
Legato
CE Service Module (SCA Profile)
Sonata
CE Wholesale Serviceability
LSO RA Project
(MEF 55.0.y)
Sonata
CE Wholesale Ordering
Network Resource Model
MEF Common Info Model
MEF Core Model Specification
MEF Papyrus
Guidelines
MEF Modeling
Guidelines
Shared SDO Core Information
Model
TMF GB922
ONF Core
6.2, 7.2, 10.3, 26.1, 28, 33, 45, 51, 54
ONF TAPI

## Slide 6: Leveraging T-API SDK Structure Considerations
Modularity
  Package functional features into small self-contained largely-independent modules
Conformity
  Standardize a single core technology-agnostic specification that abstracts all common transport network functions for the interface
Extensibility
  Facilitate exchange of diverse network information specific to different layers, technologies, standards organizations and vendors in a consistent manner using the same API core model constructs
Interoperability
  Ensure interoperability via conformance to the TAPI methodology and compliance with the core standardized TAPI spec

## Slide 7: In progress discussion - MEF Modeling aligned with ONF
Shared SDO Core Information
Model (ONF Core/TMF SID)
MEF Core Model
MEF Order Model
MEF Service Model
MEF Resource Model
Import: ONF Core
Import: TMF GB922
Import: TMF GB922 & MEF10.3
Source: ONF TAPI SERVICES
Connectivity
Service
Path Computation
Service
Virtual Network
Service
Notification
Service
Topology
Service
API IM relates to information exchanged over an interface and the entity definitions are intended to provide a logical structure for encapsulating information that is exchanged, and not intended to specify the information model patterns for implementations on either side of the interface
MEF Shared Information Context
MEF Extension Specifications
Import: ONF TAPI IM
MEF Common - Interface Profiles
PRESTO NBI
Infrastructure Control & Management
LEGATO NBI
SOF
SONATA/INTERLUDE EBI
B2B
CANTATA/ALLEGRO EBI
C2B
Network Resource Provisioning
MEF Specifications
Import: TMF API

## Slide 8: MEF 55 Entities
CIM project focus is to model MEF 55 abstractions to support LSO management of Product, Service and Resource Views
  CIM identifies relationship between leveraged TMF and ONF models
Model and Interface projects are based on CIM and share models that include attributes defined in MEF Technical Specifications
  projects identify support for MEF 55 functional requirements
  Resource View aligning with ONF TAPI model
Service View
Equipment
Element Control & Management
Service Orchestration & Infrastructure Management
(Subnetwork)
LSO RA
Context
Information Class Examples per Management Abstraction View
Service Orchestration
(Provider domains & multi-domain)
Business Apps
Product View
Network & Topology
Management
Abstractions
Resource View
Product Catalog
Product Offering
Customer
Product
Product Spec
Fabric
Network Element
Card
VNF
Link
Forwarding Domain
Forwarding Construct
Logical Termination Point
Route
Service
Service Component
Service Spec
Service Access Point
Service Interface
VNE
Port
Facility
Server
Chassis
Rack
Notes: Product View: The product domain is specific to the interaction between the Customer and the Product Offerings of a Service Provider.
Service View: A Product Instance is realized as one or more Services and associated Resources; thus Services are tightly bound to Product Instances and may be viewed to represent the Customer experience of the Product Instance that has been realized within the Service Provider’s infrastructure. <jcs> Since a Product is realized as Services AND Resources, both are “tightly bound”. But what does “tightly bound” mean? I am assuming that it acts similar to a composition, but I’m not sure.
In the SID and even ZOOM, Customer Experience is SEPARATE from Services and Resources. I think that this is a Good Thing. We’ve already corrected that in the CIM spec. </jcs>
Resource View Services are delivered via resources in the network, whether physical or logical. Physical resources are actual hardware, and logical resources can be viewed as functionality provided by specific pieces of hardware. The resource view can be further sub-divided into the Network and Topology View and the Element and Equipment View.
  The Network and Topology View encompasses all the functions across network elements, on the basis of administrative network domains.
  The Element and Equipment View pertains to the management of a specific set of devices.
<jcs> This is a long discussion. Briefly, PhysicalResource is broken if it subclasses from ManagedEntity – what is manageable about a Chassis? It is a hunk of metal.  In Zoom, we subclassed PhyscialResource from UnManagedEntity. We do differentiate between LogicalResource and VirtualResource, and both are subclassed from Resource. The MEF CIM is being changed to reflect this. </jcs>

## Slide 9: MEF 55 Entity Relationships
Product Catalog
Product
Offering
Customer
Product
Spec
Product
Service Component
Logical Termination Point
Forwarding Construct
Link
Rack
Chassis
Network Element
Card
Port
Server
Fabric
VNF
Route
VNE
Service View
Element & Equipment
Product View
Network & Topology
Resource View
Management
Abstractions
Network Function
Service Access Point
Service
Interface
Service Spec
Service
Forwarding Domain
TBD in MEF 55.x

## Slide 10: Modeling Service to Network entities
MEF 55 Service View relationship to Network View
  A Service is visible and directly usable by the Customer, but may be divided within the Service Provider's infrastructure into one or more Service Components, for instance corresponding to forwarding domains at the resource layer [Forwarding Construct is resource layer instance] or to underlying access services that the Service Provider has purchased from a Partner domain. Service Components are not visible to the Customer. Software systems implementing service related functionality have traditionally been operational support systems in the service management domain or service management systems. Note: in the TM Forum SID [TMF GB922], a Service is referred to as a Customer Facing Service (CFS) and a Service Component is referred to as a Resource Facing Service (RFS).
*Note -Although the UML from the TM Forum SID Model includes both the GB922 (classic SID objects) and the Zoom objects as independent models, the effort to align the GB922 with Zoom is outside the scope of MEF. Current approach is that MEF considers the GB922 objects for product and service constructs building a relationship to ONF constructs via a resource “placeholder” entity. MEF providing input and aligning with a shared SDO model.

## Slide 11: Service View

## Slide 12: Ethernet Service View Concepts
      “ The ETH Layer is responsible for the service view presented by the Service Provider to its Subscribers and CENs participating in the Ethernet service. It is responsible for the instantiation of Ethernet MAC oriented connectivity services and the delivery of Ethernet service frames presented across well-defined internal and external interfaces and associated reference points”.
Ethernet Service An end-to-end connection (EVC) offered by a service provider between two or more subscriber sites (UNI’s)that enables the transfer of Ethernet Service Frames between them in accordance with a specified level of quality.
Ethernet Service Type A classification of an Ethernet service based upon the topology (i.e. p2p, mp2mp, rooted mp…) of the subscriber sites and a well specified direction of Ethernet flows between sites.
Ethernet Service Component A segment of an Ethernet service that represents connectivity (OVC) between a subscriber site and a network operator (UNI/ENNI), or connectivity between network operators (ENNI/ENNI), or connectivity between a service providers internal networks (UNI/INNI, INNI/INNI).
Ethernet Service Access Point An endpoint of an Ethernet service through which Ethernet service frames are classified, metered, and marked for transit through the Carrier Ethernet Network (EVC per UNI, OVC endpoint)
Ethernet Service Interface A place of interconnection between a subscriber site and an Ethernet service provider (UNI) , or between two service providers (ENNI). A demarcation point between administrative boundaries.
Ethernet Service Specification A specification of a set of Ethernet Service attributes and their associated values that characterize an Ethernet Service, an Ethernet Service Access Point, or an Ethernet Service Interface.

## Slide 13: MEF Intra Provider Service Example
I-NNI
Aggregation
Network
I-NNI
Core
Network
Aggregation
Network
UNI
UNI
EVC
UNI (User-to-Network Interface)
  Physical interface/demarcation between service provider and subscriber
  Service start/end point
Ethernet Virtual Connection (EVC)
  Logical representation of an Ethernet service as defined by the associate between 2 or more UNIs
NNI (Network-to-Network Interface)
  Demarcation/peering point
    between service provider internal networks (I-NNI)
    between service provider networks (E-NNI) (not shown)

## Slide 14: MEF 55 – Service View (SOF)
Service
I-NNI
Aggregation
Network
I-NNI
Core
Network
Aggregation
Network
UNI
UNI
EVC
Service Component
Service Component
Service Component

## Slide 15: MEF Inter Provider Service Example
E-NNI
Operator 1
Network
E-NNI
Operator 2
Network
Operator 3
Network
UNI
UNI
EVC
UNI (User-to-Network Interface)
  Physical interface/demarcation between service provider and subscriber
  Service start/end point
Ethernet Virtual Connection (EVC)
Logical representation of an Ethernet service as defined by the association between 2 or more UNIs
Operator Virtual Connection (OVC)
  Logical representation of an Ethernet service as defined by the association between 0 to many UNIs AND 1 or more ENNIs
NNI (Network-to-Network Interface)
  Demarcation/peering point
    between service provider internal networks (I-NNI) (not shown)
    between service provider/operator networks (E-NNI)
OVC
OVC
OVC

## Slide 16: MEF 55 – Service View (SOF)
Service
Service Component
Service Component
Service Component
E-NNI
Operator 1
Network
E-NNI
Operator 2
Network
Operator 3
Network
UNI
UNI

## Slide 17: Service View MEF Core Model

## Slide 18: Proposed MEF 7.3 – Service Info Model

## Slide 19: Resource View

## Slide 20: Ethernet Resource View Concepts
      “The ETH Layer is also responsible for all service-aware processing aspects associated with the treatment of the Service Frames, including operations, administration, maintenance and provisioning capabilities [of network resources] required in support of the Ethernet services”.
Ethernet Forwarding Domain A topological component of the Eth Layer defined by a set of Eth Service EndPoints, made available for the purpose of transferring information within a given administrative portion of the ETH layer network
Ethernet Link A topological component that describes a topological relationship between Ethernet Forwarding Domains.
Ethernet Forwarding Construct The ETH layer transport entity that conveys the ETH Characteristic information (CI) between a set of two or more ETH Layer termination points in a given ETH Layer.
Ethernet LTP Service EndPoint A reference point that represents a point of transfer for connectionless traffic units between Ethernet forwarding domains.
Ethernet LTP Node EndPoint A reference point that represents a point of entry into an Ethernet Layer Network.

## Slide 21: MEF 55 - Network View (SOF)
Forwarding Construct
type=edge
Forwarding Construct
type=transit
Logical Termination Point
type=INNI
Link
VLAN Pool
Forwarding Domain
VPLS Pool
Forwarding Domain
Forwarding Domain
Id Pool
Logical Termination Point
type=INNI
Logical Termination Point
type=UNI
Link
Forwarding Construct
type=edge
Logical Termination Point
type=UNI
Logical Termination Point
type=INNI
I-NNI
Aggregation
Network
I-NNI
Core
Network
Aggregation
Network
UNI
UNI
EVC
Logical Termination Point
type=INNI

## Slide 22: Network View (ICM)
Connectivity Service (FC)
type=edge
Connectivity Service (FC)
type=transit
Link
VLAN Pool
Forwarding Domain
VPLS Pool
Forwarding Domain
Forwarding Domain
Id Pool
Link
Connectivity Service (FC)
type=edge
LPSpec = Eth
type=INNI
I-NNI
Aggregation
Network
I-NNI
Core
Network
Aggregation
Network
UNI
UNI
EVC
ServiceEndPoint (LTP)
NodeEdgePoint (LTP)
LPSpec = Eth
type=UNI
ServiceEndPoint (LTP)
NodeEdgePoint (LTP)
LPSpec = Eth
type=INNI
ServiceEndPoint (LTP)
NodeEdgePoint (LTP)
LPSpec = Eth
type=INNI
ServiceEndPoint (LTP)
NodeEdgePoint (LTP)
LPSpec = Eth
type=INNI
ServiceEndPoint (LTP)
NodeEdgePoint (LTP)
LPSpec = Eth
type=UNI
ServiceEndPoint (LTP)
NodeEdgePoint (LTP)

## Slide 23: MEF PRESTO NRP View
PRESTO

## Slide 24: Network View MEF Core Model
Forwarding Construct
Forwarding Construct
Node EndPoint
Service EndPoint

## Slide 25: ONF CORE with ONF TAPI realization

## Slide 26: ONF TAPI – Connectivity Model

## Slide 27: ONF TAPI – Endpoint Model

## Slide 28: MEF NRP/NRM – Network Model based on TAPI