## Slide 1: Use Case - 3
Multi-domain case
Xian Zhang
Huawei

## Slide 2: Mapping from Service/EVC to ForwardingConstruct Single Provider, single managed FD, partitioning
EVC (the end-to-end CarrierEthernetService)
ForwardingDomain
ForwardingConstruct
managed object classes at Service level (potentially appearing at Legato, Interlude)
managed object classes at Resource level (potentially appearing at Presto)
NE
NE
NE
NE
ForwardingConstruct
ForwardingConstruct
UNI
ForwardingDomain
UNI
LTP
LTP
E-NNI
LTP
LTP
ForwardingDomain
Link
E-NNI
Source: MEF
Issue:
UNI link: ETH; => a multi-domain, multi-layer case
Notes: UNI link: ETH; => a multi-domain, multi-layer case
This is not multi-layer use case.
  For the OTN layer this is ETH encapsulation using GFP
  For L2 layer there is L2 topology that can be based on PW.

## Slide 3
S1
S2
S3
s36
S4
S6
S37
s38
S9
S10
S11
Network domain 1
S21
S22
S23
S25
S24
S26
S27
S28
S29
S30
S31
Network domain 2
C-R1
C-R2
C-R3
C-R4
C-R5
C-R6
Customer domain 1
Customer domain 2
Network domain 3
S39
Customer domain 3
C-R7
C-R8
ODUk link
Note:
OTN-Optical layer
controlled by each domain controller
and not exposed
Via Controller NBI.
Figure provided by Igor

## Slide 4: Controlling Hierarchy
MDSC
PNC1
PNC2
PNC3
Assumption:
1: client controller knows the C-Rx and its access link information.
2: MDSC knows how to map C-Rx and its network side of nodes within its network domain.
3: MDSC has no topology information at all before each PNC reports its topology.
Network Domain 1
Network domain 3
Network Domain 2
Client Controller
Notes: How does MDSC know #2?

## Slide 5: Domain controller reporting
MDSC
PNC1
PNC2
PNC3
Domain 1 abstract TE topologies (single node)
Domain 2 abstract TE topologies
Domain 3 abstract TE topologies
NE-A
PNC1 (single node)
PNC3 (same as physical topology)
PNC2 (single node)
NE-B
NE-C
NE-A
NE-D
NE-1
Notes: Confusing with repetition of NE-A, and node names for PNC3 do not match to those in slide 3.

## Slide 6: Network Topology (teas) Model Instantiation (PNC1 to MDSC)
<networks>
<network>
network-id=Network-A, provider-id= provider PNC1, client-id= MDSC
<networks-state>
<network>
network-ref: <NW-A ref>
server-provided: true
<node>
node-id: NE-A
<termination-point>
tp-id: TP-1
<termination-point>
tp-id: …
All UNI/NNI side TPs
Changing to
a module
<termination-point>
tp-id: TP-7
<network-types>
=/te-topology/otn-topology
< underlay-topology >
Provider-id: <…>
Network-id: <….>
Client-id: <0>
<termination-point>
tp-id: …
<link>
Link-id: Link1
<link>
Link-id: Link7
<source>
src-node: <NE-A ref>
source-tp: <TP-1 ref>
<destination>
dest-node: <NULL>
dest-tp: <NULL>
< connectivity matrix>
The capability between each TP pairs
If nothing is provided, it can either be:
No constraints at all;
Path computation function of Tunnel model is expected to be used.
<external-domain>
Remote-te-node-id: <…>
Remote-te-link-tp-id: <…>
Plug-id: : <1>
<link attributes>
Total bandwidth: <100G>
Available bandwidth: NOT USED
Available ODU list: <40*ODU1, 10*ODU2, etc.>
Note:
1: PNC2 will report something similar;
2: PNC3 will report as described in use case 1(additional
intra-domain links/attributes;
Notes: Why does PNC need to know about the inter-domain links. Should it just know about the UNI, i-NNI TPs?
Who is going to program the remote link info? Mostly PNC. Rest of the info in this instance diagram is just related to node.
In the MDSC model view, which network is the parent of inter-domain links?
For node hierarchy
  There should be <te> container under node.
  <te> should contain <config>
  <config> should contain <te-node-attributes>
  <te-node-attributes> contains <underlay-topology>
For Link hierarchy:
  <te> -> <config> -> <te-link-attributes>
  Do both remote-te* and plug-id need to be used. I thought just one was required.

## Slide 7: What does MDSC get?
Domain 2 abstract TE topologies
NE-3
NE-5
NE-2
NE-4
NE-6
NE-1
C-R1
C-R2
C-R3
C-R4
C-R5
C-R6
C-R7
C-R8
MDCS merges what is gets from PNCs and generate its own view of the multi-domain topology
Note:
1) Plug-id is needed to correctly connect inter-domain nodes;
2) What if the two link capabilities are not the same?
(see next page)
Notes: The interdomain links might be provisioned top down, rather that bottom-up discovery.
What are domain controllers sending?
How does MDSC stitch different domain controller topologies?
Different ways MDSC can persist and expose network?

## Slide 8: Non-identical Link attributes
Issue: what to do when the two links reported by different PNCs do not have identical attributes?
Solution: MDSC can keep what is mutual on both links in its own TED. In this case, only setting up ODU2 or ODU4 LSP/tunnel.
Domain 1 abstract TE topologies (single node)
Domain 2 abstract TE topologies
NE-A
PNC1 (single node)
PNC2 (single node)
NE-1
Plug-id=1
Plug-id=1
Total: 100G
80*ODU0;
10*ODU2;
1*ODU4;
Total: 100G
40*ODU1;
10*ODU2;
1*ODU4;
Notes: - MDSC should have the correct info and should fix the info in PNC.

## Slide 9: MDSC – Path Computation
Domain 2 abstract TE topologies
NE-3
NE-5
NE-2
NE-4
NE-6
NE-1
C-R1
C-R2
C-R3
C-R4
C-R5
C-R6
C-R7
C-R8
Step 2: MDSC figures out the route based on its topology and it is shown in the figure.
Step 1: Client Controller sends a service request asking for a unprotected ODU tunnel/service from C-R2 to C-R6.

## Slide 10: MDSC=>PNC
MDSC
PNC1
PNC3
PNC2
Domain 1 abstract TE topologies (single node)
Domain 2 abstract TE topologies
NE-A
PNC1 (single node)
PNC2 (single node)
NE-1
Link2/tp2
Link4/tp4
Notes: Show connectivity matrix inside the NE.
Individual request coming down using the TE Tunnel model.

## Slide 11: TEAS Tunnel Model Instantiation (client => MDSC)
<te>
<tunnels>
<config>
name: Service-1
tunnel-id: tunnel-1-id
type: p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: up
<source>
Source: NE-A
<destination>
Destination: NE-A
<src-tp-id>
Source-ttp: NULL
<dest-tp-id>
Destination-ttp: NULL
<tunnel>
name: <Service-1 ref>
type: <p2p ref>
tunnel-id: <tunnel-1-id ref>
<primary-paths>
Name: <path A-ref>
<config>
type: explicit
<explicit-route-objects>
index: 0
e-r-usage: route-include-ero
type: link
link-index: <link2>
Index=1
e-r-usage: route-include-ero
Type=label
Label: <…>
Index: 2
e-r-usage: route-include-ero
type: link
link-index: <link4>
…
Label: <…>
MDSC
PNC1
PNC2
PNC3
<secondary-paths>
NULL
Issues:
If there are multiple-topologies, should the MDSC specify on which topology?
Link-index in ERO missing!
How to specify ODU label? (in ODU tunnel)
ODU tunnel: how to augment from TE Tunnel?
Is unnumbered link same as TP? (router-id + interface-id)
Notes: How to model the TP endpoint for the tunnel / Segment-tunnel? Segment tunnel depends on the view.
How is this different from single layer, single domain use case?
Why does topology need to be specified? The endpoints must be within the same topology, as this request is coming to PNC.
ODU augmentation example is part of single layer, single domain use case.
Link index, etc. for ERO can be augmented in the te-transport-model

## Slide 12
Node A
TP1
TP2
Src
Dst
Case A
Loose ERO as: NodeA/TP1 (ingress)
It will be like: Src-NodeA/TP1-NodeA/TP2-Dst
TP3
Node A
TP1
TP2
Src
Dst
Case B
Loose ERO as: NodeA/TP1 (egress)
It will be like: Src-NodeA/TP2-NodeA/TP1-Dst
TP3
Another issue: TP directionality?