## Slide 1: Transport Requirement
May 05th, 2016

## Slide 2: Network Topology & Service Constructs
Requirements

## Slide 3: Generic Requirements
[R1] User Intent: Maintain separation between high level user intent and the state in the network [Ref: OpenConfig].
  E.g. separation between user service request, including all constraints, and the actual service & connection state in the network.
[R2] State Management: Network and service objects supporting the following states [Ref: TAPI-FRS]:
  Administrative state (locked, unlocked),
  Operational state (enabled,disabled)
  Lifecycle state (Planned, Potential, Installed, In_Conflict, Pending_Removal)
[R3] Identification: Network and service object identifiers [Ref: TAPI-FRS]:
  IDs [1]
  Names[NV]
  Labels[NV]
  Extensions [NV]

## Slide 4: Network & TE Topology
[R4]: Network Topologies [Ref: TAPI-FRS]:
  Topology Retrieval:
    Allow retrieval of top-level Topology instances.
  Topology elements:
    Allow retrieval of Nodes and Links present in the topology.
  Multi-level topologies [Ref: CIM]:
    Allow retrieval of lower level topologies.
  Virtual Topologies (VTN):
    Documented in a later section

## Slide 5: Topology Link
[R5]
Support for the following Topological Links [Ref: TAPI-FRS]:
  Physical Links
  Logical / Abstract Links
  Compound Link: Internally aggregated lower-level serial/parallel links.
  Access Links: Links connecting router ports to client port of the transport system.
  Transitional Links: Links between layers.
Link attributes:
  Cost, Latency, Integrity and Capacity
  Risk characteristics including shared-risk
Link elements:
  Allow retrieval of the associated topology / virtual topology.
  Allow retrieval of associated nodes and termination points.
Layering
  Association to the underlay circuit/service, if any.

## Slide 6: Topology Node
[R6]
Support for the following Topology Nodes [Ref: TAPI-FRS, CIM]:
  Physical Node
  Logical / Abstract Node
  Chassis / Forwarding Domain (do we need this?)
Node attributes:
  Layer information
  Node Type (?)
  Node Version (?)
Node elements:
  Allow retrieval of termination points present in the node.
  Allow retrieval of the associated topology / virtual topology
Layering:
  Associations to the underlay/server nodes, if any.

## Slide 7: Termination Points
[R7]
Support for the following Termination Points [Ref: OpenConfig]:
  Physical client side TP
  Logical TP
  Optical channel TP
  Physical Line side TP
Termination Point attributes [Ref: OpenConfig]:
  Supporting equipment vendor, part, and revision

## Slide 8: Service
[R8]
Support for CRUD operations for the service
Support for Service creation and update requests with the following inputs and outputs [Ref: TAPI-FRS]:
  Service Request Inputs:
    Service ID (for service update)
    Service Type (P2P, P2MP, MP2MP)
    P2P – Uni-directional, Bi-directional
    Capacity
    Service End Points with following details:
      End Point role (root, leaf)
      Reference to the Termination Point
      Service Endpoint Layer
    Optional Constraints:
      Service Layer
      Service Level (CoS, Priority, Resiliency, Availability)
      Latency
      Cost
      Risk Characteristics (shared risk): SRLG/Diversity
      Include Path, Exclude Path (Nodes and Node Edge Points)

## Slide 9: Service
    Risk Characteristics / Protection support:
      Protection Type: UnProtected, 1+1, 1:N, etc.
    Schedule: Start & End Time
  Service Request Output:
    Service ID (for service creation)
    Service States
    Service characteristics - inputs
  Support for service notifications:
    Service lifecycle notifications: Service creation, deletion, Attribute Value Change
    State change notifications: Operational state notification
Any requirements around the following:
  Service Policies: TBD
  Service Templates: TBD

## Slide 10: Connection
[R9]
Connection creation can be triggered as part of the service creation request.
Connection creation request should use inputs provided for service creation. These inputs include the following [Ref: TAPI-FRS]:
    Service End Points with following details:
      End Point role (root, leaf)
      Reference to the Termination Point
      Service Endpoint Layer
    Capacity
    Optional Constraints:
      Service Layer
      Service Level (CoS, Priority, Resiliency, Availability)
      Latency
      Cost
      Risk Characteristics (shared risk): SRLG/Diversity
      Include Path, Exclude Path (Nodes and Node Edge Points)
    Objective function (e.g. Minimize cost, Minimize latency, etc.)

## Slide 11: Connection
  Connection Request Output:
    Connection ID
    Connection States
    Connection path
    Routing constraints that are met
  Support for connection notifications:
    Connection lifecycle notifications: Connection creation, deletion, Attribute Value Change
    State change notifications: Operational state notification
Do we need Connection to represent device cross connected / flow entry?

## Slide 12: Virtual Network (VTN)
  [R10]
  TBD

## Slide 13: Summary & Log
Requirements | Briefing | Log
[R1]: User Intent | Modeling requirements? | 
[R2]: State Management | Parameter requirements? | 
[R3]: Identification | Parameter requirements? | 
[R4]: Network Topologies | A mixture of both protocol and parameter requirements? | 
[R5]: Topology Node | Parameter requirements? | 
[R6]: topology links | Parameter requirements? | 
[R7]: topology tp | Parameter requirements? | 
[R8]: service | A mixture of both protocol and parameter requirements? | 
[R9]: connection | parameter requirements? | 
[R10]: VTN | No content yet | 

## Slide 14: Transport Use Cases
Requirements

## Slide 15: Mapping from Service/EVC to ForwardingConstruct Single Provider, single Forwarding Domain
NE
NE
EVC (the end-to-end CarrierEthernetService)
ForwardingConstruct
The MEF 7.3 UNI class represents the UNI-N architectural construct, plus some aspects of related Ethernet Link.
UNI
LTP
UNI
LTP
managed object classes at Service level (potentially appearing at Legato, Interlude)
managed object classes at Resource level (potentially appearing at Presto)
ForwardingDomain
Source: MEF

## Slide 16: Mapping from Service/EVC to ForwardingConstruct Single Provider, two FDs separately managed
NE
NE
NE
NE
EVC (the end-to-end CarrierEthernetService)
ForwardingConstruct
ForwardingConstruct
UNI
I-NNI
ForwardingDomain
UNI
LTP
LTP
I-NNI
LTP
LTP
managed object classes at Service level (potentially appearing at Legato, Interlude)
managed object classes at Resource level (potentially appearing at Presto)
ForwardingDomain
Source: MEF

## Slide 17: Mapping from Service/EVC to ForwardingConstruct Single Provider, single managed FD, partitioning
EVC (the end-to-end CarrierEthernetService)
ForwardingDomain
ForwardingConstruct
managed object classes at Service level (potentially appearing at Legato, Interlude)
managed object classes at Resource level (potentially appearing at Presto)
NE
NE
NE
NE
ForwardingConstruct
ForwardingConstruct
UNI
ForwardingDomain
UNI
LTP
LTP
I-NNI
LTP
LTP
ForwardingDomain
Link
I-NNI
Source: MEF

## Slide 18: Multi-Layer Topology Instantiation
Source: T-API FRS

## Slide 19: E2E Service in ML Topology
Source: T-API FRS

## Slide 20: Multi-layer and multi-domain

## Slide 21: Terminal Device Model
Source: OpenConfig